## Slide 1: Vehicle networks infrastructure
L08 exercise – FR intermediate

## Slide 2: Agenda
FlexRay in restbus
How to create a panel
How to test in CANoe

## Slide 3: FlexRay in restbus
V model process of development

## Slide 4: FlexRay in restbus
CANoe signal server concept
Signal server makes all of a network’s signals available
FlexRay Scheduler makes it possible to send out signals in their respective slots

## Slide 5: FlexRay in restbus
Extension for OEMs
Interaction layer
Network management
Transport protocol
*The FlexRay scheduler can be supplemented or replaced by OEM extension

## Slide 6: FlexRay in restbus
Configuration
Manual configuration
The user must make all settings manually.
FR template is available
Each node must be configured independently and individually
Configuration with wizard
Some settings are made automatically

## Slide 7: FlexRay in restbus
Resume: Manual configuration steps
Step: Create a new configuration
2. Step: Associate database
3. Step: Insert network node
4. Step: Make node allocations
5. Step: OEM extensions (optional)
6. Step: Configure network interfaces (optional)
7. Step: Configure messages
8. Step: Define Coldstart nodes
9. Step: Define Wakeup

## Slide 8: FlexRay in restbus
Resume: Wizard configuration steps
1. Step: Create new configuration with wizard
2. Step: Associate a database 3. Step: Add ECUS
4. Step: Set hardware channel
5. Step: Complete the configuration
6. Step: Define the Coldstart nodes
7. Step: Define Wakeup

## Slide 9: How to test in CANoe
CANoe tests are hierarchically organized:
Uppermost element is a Test setup
Test modules are part of a Test Environment
Test Environments are separately stored and can be used separately
Test Setup
  Test Environment
    Test Module
    Test Folder
      Test Case
      Test Group
        Test Case
          Test Step
          Test Step
      Test Group
    Test Module
  Test Environment

## Slide 10: How to test in CANoe
The Test Module is subdivided into:
Test Groups
Test Cases
Test Steps
Every Test Module has a test execution dialog for execution control. It indicates test progress and test results

## Slide 11: How to test in CANoe
A report is created during test execution
General information about the Test Environment
Versions
Test Cases and Test Steps documentation
Verdicts
Comments

## Slide 12: How to test in CANoe
Test Setup configuration
  New or existing one
CAPL Test Module configuration
  Define CAPL source code
  Activate report generation
  Define start behaviour
Implementation of:
  Test Control
  Test Cases
  Test Steps

## Slide 13: How to test in CANoe
Test Environments contain any number of Test Modules
Test Modules can be implemented in CAPL or .NET
Folders are used to group Test Modules
Test Environment can be extended by:
  Generators
  Replay blocks
  Network nodes

## Slide 14: How to test in CANoe
Every Test has its own configuration settings:
Name
Start behavior
  Immediately at measurement start
  Upon key event
  Via environment or system variable
Path and name of the CAPL source code

## Slide 15: How to test in CANoe
Test Modules can be started manually with the Test Execution Dialog
All Test Modules in a Test Environment can be executed in sequence

## Slide 16: How to test in CANoe
The most common test function
TestModuleTitle ("Functional ")
TestModulesDescription ("Functional Test")
TestModulesDescription ("involves")
testReportAddSUTInfo("Device", "CANister")
testReportAddSUTInfo ("Firmware", "%d", )
testReportAddEngineerInfo("..","..")
testReportAddSetupInfo ("CAN Interface", "")
testReportAddsetupInfo ("Serial Number", "_")
testStepFails("..","..")
testStepPass("..","..")

## Slide 17: How to test in CANoe

## Slide 18: How to test in CANoe
Examples of stimulations for the SUT (DUT)
Sending a message
Setting signals
Setting environment variables
Setting IO ports

## Slide 19: Test case workflow – waiting for
For receipt of a message
For a setting of environment variables
For a specific time period
For events of the TSL (Test Service Library)
For user-defined events
Syntax:
long testWaitFor
...Timeout
...SignalIn/OutSideRange
...SignalMatch
...ValueInput
...Message
...Syscall
... TesterConfirmation