## Slide 1: Vehicle networks infrastructure
L08 exercise – FR intermediate

## Slide 2: Agenda
FlexRay in restbus
How to create a panel
How to test in CANoe

## Slide 3: Exercise feedback
Exercise 1
Create a new configuration
  Insert the FIBEX file VectorCar-FIBEX 31.xml
  Save your configuration.
Insert the following nodes in your Simulation Setup.
  KeyunitECU, Engine ECU, GearboxECU
  Your assigned Trainee ECU node (1-8)
Execute a measurement
  Switch CANoe to simulate mode
  Start your measurement and observe the Trace window
  Check whether all messages have been sent correctly.
Check the following properties of the messages
  Which messages are sent out as startup/sync frames
  Are the signals for the training model available in the messages

## Slide 4: Exercise feedback
Exercise 1 – part 2
The task is to manipulate the sigIgnition signal with the Symbol and Node Panel.
Open the Symbol Panel for the sigIgnition signal.
Open the Node Panel for the KeyunitECU.
Manipulate the signal values from zero to three and observe the changes in the Trace window.

## Slide 5: Exercise feedback
Exercise 2
The task is to manipulate the sigEngineSpeed signal with a signal generator.
Configure the signal generator
  Open the configuration for the signal generators,
  Insert a signal generator for the sigEngineSpeed signal.
Simulate a ramp that has the following properties:
  The signal value should rise from 0 to 8000
  The period length of the signal is 5 seconds

## Slide 6: Exercise feedback
Exercise 3
The task is to create a panel that displays the sigEngine Speed signal and enables manipulation of the sigGear signal.
Creating a new Panel
  Open the Panel Designer and create a new panel
  Save the panel as Exercise3.xvp.

## Slide 7: Exercise feedback
Exercise 3 – part 2
Display of sigEngine Speed
  Insert a display element for the signal
  Assign the signal to the display element
  Save the panel and check its functionality
Manipulating sigGear
  Insert a slider element for the signal
  Assign the signal to the slider element
  Save the panel and check its functionality