## Slide 1: Vehicle networks infrastructure
L03 exercise – CAN bus – Basic

## Slide 2: CAN bus – Basic
Available databases:
DBC – Data Base for CAN
LDF – LIN Description File
FIBEX – Field Bus Exchange Format (FlexRay, MOST, CAN, TTCAN, LIN and Ethernet)
ARXML – AutoSAR XML (FlexRay, MOST, CAN, TTCAN, LIN and Ethernet)

## Slide 3: Exercise feedback
Task 1
Create a new one or continue with the existing one .dbc file.
A message shall contain 5 signals
  2 signals shall be signed – 8 bits long
  2 signals shall be unsigned – 8bits long
  1 signal shall be float
Add a raw to physical conversion for one of the listed signals

## Slide 4: Exercise feedback
Task 2
Create 5 additional signals
  Datatype should be the same as in the previous task
Create a new message and define created signals
  All signals as well as messages should be added to the receiver list
  Message and signals should be in the list of received signals and messages of the already created network node
  Mapping of the received signals and messages must be done only mapping of existing signals
  Based on the mapped reception signal, the tool will automatically add the message to which the selected signal belongs to the list of reception messages
Notes: In order to map the reception signal to the desired network node, it is necessary to select the Edit option from the menu obtained by right-clicking on the network node, as shown in the picture on the left below.
after selecting the Mapped Rx Sig. and pressing the button Add.. opens a new window with a list of signals, shown in the image on the upper right. After selecting the received signals and confirming with the OK button, the selected signal as well as the message in which the signal is defined will be visible in the list of received signals and messages of the network node.

## Slide 5: Exercise feedback
Task 3
Add one new network node
The messages and signals that were defined as receiving for the previous node should be defined as transmitting for the new node.
The messages and signals that were defined as transmitting for the previous node should be defined as receiving for the new node.
Do consistency check